## Slide 1: Mathematical Operations
Base 2: the native base for computer systems
Glyphs: 0, 1
On a computer, we are limited to a certain number of digits.
Recall, the results are summarized via the use of status flags.
  For unsigned operations:
    the final value is Zero (Z)
    the calculation resulted in final carry (C)
  For signed values
    the final value is Negative (S)
    the calculation resulted in an overflow (V)

## Slide 2: Binary Addition:
We have only two digits
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = ?
What do we do in base 10
  9 + 9 = ?
+ |  | B | 
 |  | 0 | 1
A | 0 | 0 | 1
 | 1 | 1 | ?
Base 2
Base 10
1
9
+
8
9

## Slide 3: Binary Addition (1-digit):
We have only two digits
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = 10
What do we do in base 10
  9 + 9 = 18
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
+ |  | B | 
 |  | 0 | 1
A | 0 | 00 | 01
 | 1 | 01 | 10
Base 2
Base 10
9
+
9
Half Adder

## Slide 4: In Binary (before)
1
1
0
1
0
0
1
1
+
?
?
C
V
S
Z
1
0
1
1
0
1
1
0
+
?
?
C
V
S
Z
C | A | B | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
C + A + B = C, S
0
1
1
0
0
0
1
1
+
?
?
C
V
S
Z
C | A | B | C | S
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
C + A + B = C, S
0
1
0
0
1
0
1
1
+
?
?
C
V
S
Z

## Slide 5: In Binary (after)
1
1
0
1
0
0
1
1
0
0
0
0
+
1
?
?
1
C
V
S
Z
1
0
1
1
0
1
1
0
0
0
0
1
+
1
1
?
0
C
V
S
Z
1
1
1
0
1
1
0
0
1
1
0
0
C | A | B | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
C + A + B = C, S
0
1
1
0
0
0
1
1
+
0
?
?
0
C
V
S
Z
1
0
1
0
C | A | B | C | S
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
C + A + B = C, S
0
0
0
0
0
1
0
0
1
0
1
1
+
0
?
?
0
C
V
S
Z
1
1
1
1
1
1

## Slide 6: Binary Addition: Practice
+
?
?
C
V
S
Z
+
?
?
C
V
S
Z
1
1
1
0
C | A | B | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
C + A + B = C, S
0
1
1
1
0
0
1
1
+
0
?
?
0
C
O
S
Z
1
0
0
1
C | A | B | C | S
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
C + A + B = C, S
1
1
1
0
0
1
1
1
0
0
1
1
+
1
?
?
0
C
V
S
Z
1
0
0
1
1
0

## Slide 7: Binary Subtraction (via Borrow)
Traditional Method ⇒
  Notice the extra squares
  Notice the extra bookkeeping
  10 - 6 = 4
Recall Method of Complements
  allows us to leverage binary addition
  need a method to encode negative numbers
A |  | B | V
0 | 0 | 0 | 0
0 | 0 | 1 | x
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | x
1 | 0 | 1 | 1
1 | 1 | 0 | x
1 | 1 | 1 | x
A - B = V
1
0
0
0
1
0
1
0
0
1
0
1
0
-

## Slide 8: Binary Subtraction (via Borrow)
Traditional Method ⇒
  Notice the extra squares
  Notice the extra bookkeeping
  10 - 6 = 4
Recall Method of Complements
  allows us to leverage binary addition
  need a method to encode negative numbers
A - B = V
1
0
0
0
1
0
0
0
0
1
0
0
0
1
0
1
1
0
0
0
-
A |  | B | V
0 | 0 | 0 | 0
0 | 0 | 1 | x
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | x
1 | 0 | 1 | 1
1 | 1 | 0 | x
1 | 1 | 1 | x

## Slide 9: Recall: Method of Complements
A technique to encode both positive and negative numbers
  uses the same algorithm to perform addition
  subtraction perform my addition of complements
Complement: a thing that completes or brings to perfection
Radix 10: (the radix or base is the number of unique digits to represent a number)
  10's complement
    7 + x = 10 : x is the 10s complements of 7 x = 3
    46 + y = 100 : y is the 10s complements of 46 y = 54
  9's complement
    7 + a = 9 : a is the 9s complements of 7 a = 2
    46 + b = 99 : b is the 9s complements of 46 b = 53
The math:
45
- 11
34
45
+ 89
134
45
+ 88
133 + 1 = 134
10's complement
9's complement
2nd Grade
V | ~V
0 | 1
1 | 0

## Slide 10: Method of Complements
A technique to encode both positive and negative numbers
MSB used to denote the sign bit (0 positive, 1 negative)
Table assumes a 4-bit represent
Use 1's complement to represent negative numbers
Divide the number range in half
Encode a positive and a negative value for each number
Pros/cons:
  ease to compute
  positive and negative representations of zero
Use 2's complete to represent negative numbers
Hold Zero as special
Fold the resulting range to assign values
Pros/cons:
  Not symmetric: extra negative number
  Need to flip all bits and ad one to form the negative number
  Consider then the predecessor of -7
 | Positive | Negative
0 | 0000 | 1111
1 | 0001 | 1110
2 | 0010 | 1101
3 | 0011 | 1100
4 | 0100 | 1011
5 | 0101 | 1010
6 | 0110 | 1001
7 | 0111 | 1000
8 |  | 
1's Complement
-1
-1
-1

## Slide 11: Method of Complements
A technique to encode both positive and negative numbers
MSB used to denote the sign bit (0 positive, 1 negative)
Table assumes a 4-bit represent
Use 1's complement to represent negative numbers
Divide the number range in half
Encode a positive and a negative value for each number
Pros/cons:
  ease to compute
  positive and negative representations of zero
Use 2's complete to represent negative numbers
Hold Zero as special
Fold the resulting range to assign values
Pros/cons:
  Not symmetric: extra negative number
  Need to flip all bits and add one to form the negative number
  Consider then the predecessor of -8: -8, -7, -6, … 0, 1, … 7
 | Positive | Negative
0 | 0000 | 
1 | 0001 | 1110 + 1 = 1111
2 | 0010 | 1101 + 1 = 1110
3 | 0011 | 1100 + 1 = 1101
4 | 0100 | 1011 + 1 = 1100
5 | 0101 | 1010 + 1 = 1011
6 | 0110 | 1001 + 1 = 1010
7 | 0111 | 1000 + 1 = 1001
8 |  | 1000
2's Complement
-1
-1
-1
-1

## Slide 12: Comparison of 1's and 2's Complement Encodings
 | Positive | Negative
0 | 0000 | 1111
1 | 0001 | 1110
2 | 0010 | 1101
3 | 0011 | 1100
4 | 0100 | 1011
5 | 0101 | 1010
6 | 0110 | 1001
7 | 0111 | 1000
 | Positive | Negative
0 | 0000 | 
1 | 0001 | 1110 + 1 = 1111
2 | 0010 | 1101 + 1 = 1110
3 | 0011 | 1100 + 1 = 1101
4 | 0100 | 1011 + 1 = 1100
5 | 0101 | 1010 + 1 = 1011
6 | 0110 | 1001 + 1 = 1010
7 | 0111 | 1000 + 1 = 1001
8 |  | 1000
1's Complement
2's Complement

## Slide 13: Status Flags Explained!
Example: 13 - 9 ⇒ 01101 + 10111 * 9: 01001 -- -9 : 10110 + 1 = 10111
C: Carry Flag
  the last step resulted in a carry value of 1
V: Overflow Flag
  the next to the last step resulted in a carry value of 1
S: Sign Flag
  the MSB in the result is set (i.e., a 1)
Z: Zero Flag
  all bits in the result are cleared (i.e., 0)
1
1
0
1
0
1
1
1
0
1
0
0
+
1
1
1
0
1
0
1
0
1
1
1
0
0
C
V
S
Z
C
V
S
Z

## Slide 14: Algorithm: Subtraction via 1's Complements
Example: 13 - 9 ⇒ 0013 + - 0009
Convert 13 and 9 into binary (01101 & 01001)
Take the 1's complement of the subtrahend (9)
  01001 → 10110
Add the complement to the minuend
Drop the leading "1"
Add 1
Optimization: introduce initial carry in
+
+
1
+
1
C
V
S
Z

## Slide 15: Algorithm: Subtraction via 2's Complement
Example: 13 - 9 ⇒ 00013 + - 0009
Encode 13 and 9 into binary (01101 & 01001)
Take the 2's complement of the subtrahend (9)
  01001 → 10110 + 1 = 10111
Add the complement to the minuend
Drop the leading "1", i.e., the carry bit.
Providing the answer:
Optimization: Addition of adding one is baked in!
+
0
C
V
S
Z

## Slide 16: Algorithm: Subtraction via 2's Complement
Example: 13 - 9 ⇒ 0013 + - 0009
Encode 13 and 9 into binary (01101 & 01001)
Take the 2's complement of the subtrahend (9)
  01001 -> 10110 + 1 = 10111
Add the complement to the minuend
Drop the leading "1", i.e., the carry bit.
Providing the answer: 4
Optimization: Addition of adding one is baked in!
1
1
0
1
0
1
1
1
0
1
0
0
+
1
1
1
0
1
0
1
0
1
1
C
V
S
Z

## Slide 17: Practice: Addition and Subtraction
Steps:
transform the operation to addition
convert abs(X) to binary
encode both numbers in 2's complement
perform binary addition
convert result to decimal
  if negative result: compute 2's complement first
8 + 9 = 17
7 - 4 = 3
-5 + 2 = -3
-16 - 3 = -19
-25 - 4 = -29 => (-25) + (-4)
1
0
0
0
0
0
1
1
+
1
0
1
1
0
1
1
1
1
0
1
1
1
1
1
0
0
1
1
1
0
C
V
S
Z

## Slide 18: Practice: Addition and Subtraction
Steps:
transform the operation to addition
convert abs(X) to binary
encode both numbers in 2's complement
perform binary addition
convert result to decimal
  if negative result: compute 2's complement first
8 + 9 = 17
7 - 4 = 3
-5 + 2 = -3
-16 - 3 = -19
0
0
0
0
+
0
1
0
0
0
0
2. 8: 001000, 9: 001001 3. 5. 17
1
0
0
0
1
0
0
1
C
V
S
Z

## Slide 19: Practice: Addition and Subtraction
Steps:
transform the operation to addition
convert abs(X) to binary
encode both numbers in 2's complement
perform binary addition
convert result to decimal
  if negative result: compute 2's complement first
8 + 9 = 17
7 - 4 = 3
-5 + 2 = -3
-16 - 3 = -19
1
0
0
0
0
0
1
1
+
1
0
1
1
0
0
1
1
0
2. 7: 000111, 4: 000100 3. -4: 111011+1 ⇒ 111100 5. 3
0
1
1
1
1
1
0
0
C
V
S
Z

## Slide 20: Practice: Addition and Subtraction
Steps:
transform the operation to addition
convert abs(X) to binary
encode both numbers in 2's complement
perform binary addition
convert result to decimal
  if negative result: compute 2's complement first
8 + 9 = 17
7 - 4 = 3
-5 + 2 = -3
-16 - 3 = -19
0
1
0
0
1
1
0
1
+
0
1
1
0
0
0
0
1
1
2. 5: 000101, 2: 000010 3. -5: 111010+1 ⇒ 111011 5. 000010+1 ⇒ 000011 = -3
0
0
1
0
1
0
1
1
C
V
S
Z

## Slide 21: Practice: Addition and Subtraction
Steps:
transform the operation to addition
convert abs(X) to binary
encode both numbers in 2's complement
perform binary addition
convert result to decimal
  if negative result: compute 2's complement first
8 + 9 = 17
7 - 4 = 3
-5 + 2 = -3
-16 - 3 = -19
0
0
0
0
1
1
0
1
+
1
0
1
0
1
1
1
1
1
2. 16: 010000 3: 000011 3. -16: 110000 -3: 111101 5. 010010+1 ⇒ 010011 = -19
0
0
0
0
1
1
0
1
C
V
S
Z