## Slide 1: mjqqt

## Slide 2: Cesare Cipher
A simple way to encode a “message”
CC-5 [ D(x) = (x – n) mod 26, where n = 5 ]
A | B | C | D | E | F | G | H | I | J | K | L | M | N | O | P | Q | R | S | T | U | V | W | X | Y | Z
f | g | h | I | j | k | l | m | n | o | p | q | r | s | t | u | v | w | x | y | z | a | b | c | d | e
m | j | q | q | t
plain
cipher

## Slide 3
00000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000010101010101010101010101010101010101010101010101010101010101010110011110000000110001100000100000000101101100011100011110000000110001100000100000000101101100011100000000000000000xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000

## Slide 4: Introduction to Encodings
Today's Plan
  Communication and Bits
  Discussions on Functions and Mappings
  Binary Strings and Fields: IPv4 and MIPS Instructions
  Fixed-length Binary Encodings
    3 bits: Octal Encoding
    4 bits: Hexadecimal Encoding
    5 bits: MIPS Register Encoding
    6 bits: Base64 Encoding, MIPS Operations and Functions Encoding
    8 bits: ASCII (text) encoding
  Variable Length Instructions: UTF-8

## Slide 5: Recall: OSI and TCP/IP
Layer | Name | Example Protocol | Naming | Transported | Hardware Device
7 | Application | http | url | data | 
6 | Presentation | --- |  |  | 
5 | Session | --- |  |  | 
4 | Transport | TCP/IP | socket | segment | 
3 | Network / Internet | IPv4 IPv6 | IP | packet | router
2 | Data Link / Link | Ethernet | MAC | frame | switch
1 | Physical | 802.11g | Interface | symbols | hub, bridge
Host layers
Media layers

## Slide 6: Communication and Bits:
Layer 1
Layer 2
Payload Header: Layer 3
Payload

## Slide 7: Decoding the Message (chunk the bits into fields)
00000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000010101010101010101010101010101010101010101010101010101010101010110011110000000110001100000100000000101101100011100011110000000110001100000100000000101101100011100000000000000000xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000000
Inter-Packet Gap, Preamble, and Start of Frame:
  00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000
  10101010 10101010 10101010 10101010 10101010 10101010 10101010
  10101011
Mac Address: 3c:06:30:40:2d:8e
  0011 1100 : 0000 0110 : 0011 0000 : 0100 0000 : 0010 1101 : 1000 1110
  0011 1100 : 0000 0110 : 0011 0000 : 0100 0000 : 0010 1101 : 1000 1110
Length: 0000 0000 0000 0000
Payload:
CRC: xxxx xxxx xxxx xxxx xxxx xxxx xxxx xxxx
Inter-Packet Gap
  00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00000000

## Slide 8: Types of Encodings
String of bits:
  Inter-Packet Gap, Preamble, Start of Frame
Binary:
  Flags: Reserved, Don't Fragment, More Fragments
Integer:
  Length, Version Number, TTL, etc.
Index:
  Protocol Lookup Table
MAC Address: 3c:06:30:40:2d:8e
  0011 1100 : 0000 0100 : 0011 000 : 0100 0000 : 0010 1101 : 1000 1110
  Hexadecimal -> Binary
IP Address: www.csun.edu
  Dotted Decimal Notation: 130.166.238.19
  1000 0010 . 1010 0110 . 1110 1110 . 0001 0011
  Decimal -> Binary
Data: (follows the IPv4 header)
  text, images, video, audio, colors, etc.

## Slide 9: Mappings and Functions
Mapping: defines a relationship
Function: a binary relation between two sets
  Encode: input -> output
  Decode: output -> input
A table can represent a function
a
0x61
97
{
123
0x7B
characters
decimal numbers
hexadecimal numbers
INPUT | OUTPUT 1 | OUTPUT 2
5 | 8 | 53
2 | 5 | 50
4 | 7 | 52
9 | ? | ?
h | ? k | 104 ? 104
0 1 2 3 4 5 6 7 8 9
a b c d e f g h i j k l

## Slide 10: Encoding Examples:
Fixed Length Lookup Tables: e.g., 0100 0011 0110 0001 0111 0100
  Octal (3 bit chunks): 020660564 010 000 110 110 000 101 110 100
  Binary Coded Decimal (4 bit chunks): 436,174 0100 0011 0110 0001 0111 0100
  Hexadecimal (4 bit chunks) : 0x436174 0100 0011 0110 0001 0111 0100
  Base64 (6 bit chunks): Q2F0 010000 110110 000101 110100
  ASCII (8 bit chunks): Cat 01000011 01100001 01110100
  MIPS Instruction (32 bit chunks): add $t0,$t1,$t2 0000 0001 0100 1011 0100 0000 0010 0000
Various Lengths: (function used to perform the mapping)
  short int (16 bit chunks): -32,768 … 32,767
  int (32 bit chunks): -2,147,483,648 … 2,147,483,647
  long int (64 bit chunks): −9,223,372,036,854,775,808 … 9,223,372,036,854,775,807
Variable Length:
  UTF-8
    Unicode Transformation Format
    1 byte to 4 bytes used to encode each character

## Slide 11: BCD: Binary Coded Decimal
Encoding of: 6 & 7
An encoding for numbers, where precision is required
Four bits are used to encode each digit
Addition is performed on each 4-bit chunk (nibble)
N | Code | N | Code
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 |  | 1010
3 | 0011 |  | 1011
4 | 0100 |  | 1100
5 | 0101 |  | 1101
6 | 0110 |  | 1110
7 | 0111 |  | 1111
0
1
1
0
6
7
0
1
1
1

## Slide 12: BCD: Addition
Addition performed on the nibble level: 6+7
N | Code | N | Code
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 |  | 1010
3 | 0011 |  | 1011
4 | 0100 |  | 1100
5 | 0101 |  | 1101
6 | 0110 |  | 1110
7 | 0111 |  | 1111
0
1
1
1
0
1
1
0
1
1
0
0
1
1
0
1
+
0
1
1
0
+
0
0
1
1
0
if (overflow or invalid code ) then
1
6
7
jump 6
0
0
0
1

## Slide 13: BCD: Addition Example: 246 + 127= 373
N | Code | N | Code
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 |  | 1010
3 | 0011 |  | 1011
4 | 0100 |  | 1100
5 | 0101 |  | 1101
6 | 0110 |  | 1110
7 | 0111 |  | 1111
0
0
0
1
0
0
1
0
0
1
1
1
0
1
1
1
0
0
0
1
1
0
1
1
1
0
0
1
0
1
0
0
1
0
0
1
0
0
0
1
1
0
0
0
0
0
+
0
1
1
0
0
1
1
1
1
0
1
0
1
1
0
0
1
1
0
0
1
1
0
+?
1

## Slide 14: Instruction Encoding: MIPS
(6 bits) The operation to be performed (MIPS Encoding)
  It also indicates the encoding format to be used!
  There are three primary formats: R, I, and J.
Other fields determine
  (5 bits) which registers are used (Register Encoding)
    rs: first source register
    rt: second register
    rd: destination register
  (5 bits) the amount a value is shifted (range: 0 .. 31)
  (6 bits) the mathematical function to be performed (MIPS Encoding)
  (16 bits) the immediate value (range: -2048 .. 2047)
  (26 bits) the address / 4

## Slide 15: Instruction Encoding: MIPS
Three primary instruction encodings include:
  R-type (register)
    for instructions using only registers
    example: 0x014b4020 (2# 0000 0001 0100 1011 0100 0000 0010 0000)
    for: add $t0, $t1, $t2 ($t0 = $t1 + $t2)
  I-type (immediate)
    for instructions with immediate values:
    example: 0x21280005 (2# )
    for: addi $t0, $t1, 5 ($t0 = $t1 + 5)
  J-type (jump)
    for instructions that perform unconditional jumps
    example: 0x0810000 (2# )
    for: j label # goto label = 0x00400000

## Slide 16: An Encoding for the Keyboard
Look at your keyboard.
  a-z, A-Z, 0-9, !@#$%^&*()_+-~`,./<>?;':"[]\{}|
  don't forget: space, tab, return, and delete key
  plus we need other stuff:
  All total, we we have 128 things to encode (2^n <= 128, what is the value of n? 7)
We need to devise an encoding that maps everything to numbers
How many bits do we need? How many things do we bits in a byte?
An example of a fixed-width encoding!
Let's build a table! Keyboard Table
ASCII, abbreviated from American Standard Code for Information Interchange, is a character encoding standard for electronic communication.

## Slide 17: Parity Bit (or Check Bit)
We are only using 7 of the 8 bits, what shall we do with it.
Algorithm (odd)
  count the number of 1's
  add a 1 to make odd
  transmit
  receive
  count the number of 1's
  if even, ask for the data to be resent
Checksum: * performs integrity checking at an aggregate level * reliability of networks have greatly improved since way back when!

## Slide 18: Extended ASCII and UTF-8 (unicode)
We could use that bit to encode more stuff: 0..255
But we have even more stuff. Let's use 16 bits to encode: 0..64K
But now we have doubled what we need to send..
Enter variable-length encoding.
  Send only a byte for the most common symbols
  Use the MSB to indicate a variable length encoding
UTF-8: encodes >2,000,000 (2^21) values, using a maximum of 4 bytes
Defines four type of bytes:
  ASCII byte: begins with a 0 (1-byte indicator)
  Continuation byte: begins with a 10
  2-byte Indicator: begins with a 110
  3-byte Indicator: begins with a 1110
  4-byte Indicator: begins with a 11110
A: |||| |||| ||||
S: |

## Slide 19: Extended ASCII and UTF-8
The list of UTF-8 characters:
Layout of the bits:
Example on how to lay it out: