## Slide 1: Lecture
Last time:
  Boolean Algebra ⇔ Digital Circuits
    Point: We can do a lot with just Combinational logic -- all true functions can be evaluated
    Point: Digital Circuits can be built to evaluate all of these functions.
  All we need is And (*), Or (+) and Not (')
  Truth Table → Boolean Algebra
  Boolean Algebra → Circuits → Boolean Algebra
  Minimization of Circuits
    Algebraic Transformations:
    Karnaugh Maps
Today: More Combinational Circuits

## Slide 2: Combinational Logic
Using just is tedious: AND (*), OR (+), NOT (')
Solution: Build components and reuse!
  XOR: A ⊕ B is equivalent to (A + B) * (A' + B')
  Half-Adder: S = A ⊕ B, C = A * B
Bigger components and with more bits!
  Binary Addition
  Binary Subtraction
  BCD Addition
  Decoder
  Multiplexer
A
B
XOR:
A | B | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 3: 4-bit Bitwise AND
R = A & B
For a n-bit operation,
  create n-duplicates of the base circuitry
  layout duplicates in parallel
  package it up
4-bit AND
 | 1 | 0 | 1 | 1 | A
& | 0 | 1 | 1 | 0 | B
 | 0 | 0 | 1 | 0 | R
 | A3 | A2 | A1 | A0 | 
 | 1 | 0 | 1 | 1 | 
 | B3 | B2 | B1 | B0 | 
 | 0 | 1 | 1 | 0 | 
 | 0 | 0 | 1 | 0 | R

## Slide 4: 1-bit Binary Addition
Recall:
  Cin + Ax + Bx → S, Cx+1
 | 1 | 0 |  | 1 | A
+ | 0 | 1 |  | 1 | B
 |  |  |  |  | S
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 5: 4-bit Binary Addition
half-adder
Recall:
  Cin + Ax + Bx → Cout, Sx
Half-Adder is not sufficient! We need a Full-Adder
 | 1 | 0 | 1 | 1 | A
+ | 0 | 1 | 1 | 0 | B
 |  |  |  |  | S
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Cin
Cout
S
A
B

## Slide 6: Full Adder
Cout = AB + Cin(A⊕B)
S = Cin⊕A⊕B
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cin
A
B
S
Cout
half-adder
Got It? Any Questions

## Slide 7: Full Adder
Cout = C'AB +
C'AB
Use Sum of Products
C
A
B
half-adder
S
Cout
Note: Renamed Cinto be C
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 8: Full Adder
Cout = C'AB + CA'B + CAB' + CAB
C'AB
CA'B
CAB'
CAB
Use Sum of Products
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 9: Full Adder
Cout = C'AB + CA'B + CAB' + CAB
Cout = C'AB + CAB + CA'B + CAB'
C'AB
CA'B
CAB'
CAB
Use Commutative Property
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 10: Full Adder
Cout = C'AB + CAB + CA'B + CAB'
Cout = (C' + C)AB + CA'B + CAB'
C'AB
CA'B
CAB'
CAB
Use Distributive Property
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 11: Full Adder
Cout = (C' + C)AB + CA'B + CAB'
Cout = (true)AB + CA'B + CAB'
C'AB
CA'B
CAB'
CAB
Use Complement Property
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 12: Full Adder
Cout = (true)AB + CA'B + CAB'
Cout = AB + CA'B + CAB'
C'AB
CA'B
CAB'
CAB
Use Identity Property
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 13: Full Adder
Cout = AB + CA'B + CAB'
Cout = AB + C(A'B + AB')
C'AB
CA'B
CAB'
CAB
Use Distributive Property
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 14: Full Adder
Cout = AB + C(A'B + AB')
Cout = AB + C(A⊕B)
C'AB
CA'B
CAB'
CAB
A ⊕ B ⇔ A'B + AB'
Cin
A
B
S
Cout
Cin | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 15: Full Adder
Cout = AB + C(A⊕B)
S = C'A'B + C'AB' + CA'B' + CAB
C'A'B
C'AB'
CA'B'
CAB
C | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cin
A
B
S
Cout
C'A'B + C'AB' + CA'B' + CAB
Sum of Products:
A ⊕ B ⇔ A'B + AB'

## Slide 16: Full Adder
Cout = AB + C(A⊕B)
S = C'A'B + C'AB' + CA'B' + CAB
S = C⊕A⊕B
C'A'B
C'AB'
CA'B'
CAB
Cin
A
B
S
Cout
C'A'B + C'AB' + CA'B' + CAB = C'(A'B + AB') + C(A'B' + AB) = C'(A⊕B) + C(A⊕B)' = C⊕(A⊕B) = C⊕A⊕B
Sum of Products:
A ⊕ B ⇔ A'B + AB'
C | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 17: Full Adder
Cout = AB + Cin(A⊕B)
S = Cin⊕A⊕B
Cin
A
B
S
Cout
Note: Renamed C to be Cin
S
Cout
AB
Cin(A⊕B)
A⊕B
Cin
C | A | B | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 18: 4-bit Binary Addition (aka: 4-bit Full Adder)
 | 1 | 0 | 1 | 1 | A
+ | 0 | 1 | 1 | 0 | B
 |  |  |  |  | S
 | 0 | 1 | 1 | 0 | B
 | 1 | 0 | 1 | 1 | A
Full Adder
Full Adder
Full Adder
Full Adder
S0
S1
S2
S3
A0 B0
A1 B1
A2 B2
A3 B3
0
Cout
Cin

## Slide 19: Binary Subtractor
Recall: A - B
  A + (2's complement of B)
  A + (1's complement of B) + 1
4-bit Binary Subtractor
Full Adder
Full Adder
Full Adder
Full Adder
Full Adder
A
B
1
S
C
S0
S1
S2
S3
A0 B0
A1 B1
A2 B2
A3 B3
1
C

## Slide 20: 4-bit BCD Addition
BCD: 35 + 28
Perform Regular Binary Addition, but account for the invalid patterns
Add six upon whenever you are in the deadzone or there is overflow
  Invalid = S3 * ( S2 + S1 )
  Overflow = Cout
# | Encoding S3S2S1S0 |  | Encoding S3S2S1S0
0 | 0 0 0 0 | 8 | 1 0 0 0
1 | 0 0 0 1 | 9 | 1 0 0 1
2 | 0 0 1 0 |  | 1 0 1 0
3 | 0 0 1 1 |  | 1 0 1 1
4 | 0 1 0 0 |  | 1 1 0 0
5 | 0 1 0 1 |  | 1 1 0 1
6 | 0 1 1 0 |  | 1 1 1 0
7 | 0 1 1 1 |  | 1 1 1 1
 | 0 | 1 | 1 | 1 | 
 | 0 | 0 | 1 | 1 | 3
+ | 0 | 0 | 1 | 0 | 2
 | 0 | 0 | 0 | 0 | 
 | 0 | 1 | 0 | 1 | 5
+ | 1 | 0 | 0 | 0 | 8
i n v a l i d
35 + 28

## Slide 21: 4-bit BCD Addition
 | 0 | 1 | 1 | 0 | 6
+ | 0 | 1 | 0 | 1 | 5
Full Adder
Full Adder
Full Adder
Full Adder
S0
S1
S2
S3
A0 B0
A1 B1
A2 B2
A3 B3
0
Cout
Full Adder
Full Adder
Full Adder
Full Adder
S0
S1
S2
S3
S0 0
S1
S2
S3 0
0
 | 0 | 0 | 1 | 0 | 2
+ | 0 | 1 | 0 | 1 | 5
Invalid = S3 * ( S2 + S1 )
Overflow = Cout
if 0 then add 0: 0000 if 1 then add 6 : 0110
CISC -versus- RISC
Cout